## Slide 1
PhD THESIS DEFENSE
Ray Tracing-Based Urban
Propagation Modelling
Sionna RT 2.0 | Ofcom 2018 Nottingham | 915 MHz and 1802 MHz
[Author Name] | [University] | 2026

## Slide 2
Presentation Outline
OVERVIEW
1
Research Context
2
Dataset & Scene Building
3
Vegetation Modelling
4
RT Configuration
5
Calibration Methodology
6
Results: 915 MHz
7
Results: 1802 MHz
8
Conclusions & Future Work

## Slide 3
Why Ray Tracing for Propagation Prediction?
MOTIVATION
Empirical Models
Fast but location-generic
No spatial resolution
Cannot adapt to scene
Limited to training environments
Ray Tracing
Physics-based prediction
Full geometry-awareness
Calibratable to measurements
Multi-path / diffraction support
Sionna RT 2.0
GPU-accelerated (DrJIT)
Differentiable renderer
Open-source (NVIDIA)
Diffraction + scattering

## Slide 4
Research Objectives
OBJECTIVES
1
Build a high-fidelity 3D urban scene from open geodata (OSM, EA LiDAR, OS OpenData)
2
Calibrate ITU-R P.2040-2 material parameters against 915 MHz field measurements
3
Evaluate RT performance across distance ranges and scene feature sets
4
Assess vegetation modelling strategies: disc geometry, Weissberger, nDSM sources

## Slide 5
Ofcom 2018 Nottingham Measurement Campaign
DATASET
1,200+
RX Measurement Locations
915 MHz
1802 MHz
TX at western high ground, 79.2 m ASL
Urban Nottingham, UK
CRS: EPSG:27700 (British National Grid)
Bias-corrected path loss measurements
Scene Coverage
West:
-1.268 deg
East:
-1.120 deg
South:
52.943 deg
North:
53.003 deg
Extent:
~14 km x 7 km
Centre elev.:
50.55 m ASL
TX height:
79.2 m ASL (+17 m AGL)

## Slide 6
End-to-End Methodology
METHODOLOGY
Geodata
Sources
OSM, EA LiDAR
DTM/DSM,
OS OpenData
Scene
Builder
Python notebook
PLY mesh gen
XML assembly
Sionna RT
2.0
PathSolver
ITU-R materials
Diffraction
Calibration
Powell optimiser
ITU material params
30 DoF
Evaluation
R², RMSE, Bias
vs measurements
208-767 RX

## Slide 7
Scene Building Pipeline
SCENE BUILDER
Data Sources
OS OpenData / OSM
Building footprints, road polygons, land use
EA LiDAR DTM/DSM
1m resolution terrain + surface model
nDSM = DSM - DTM
Vegetation height extraction (>=2m threshold)
CRS: EPSG:27700 (British National Grid), always_xy=True
Output PLY Files
terrain.ply
road_itu_asphalt.ply
bld_itu_brick.ply
water_itu_water.ply
bld_itu_concrete.ply
veg_itu_vegetation.ply
bld_itu_glass.ply
trees_itu_vegetation.ply
bld_itu_metal.ply
ndms_veg_extra.ply
bld_itu_wood.ply
terrain_veg.ply

## Slide 8
Scene Feature Set
SCENE FEATURES
Feature | Material | Notes
Terrain (DTM) | itu_wet/dry_ground | 1000x1000 grid, 10m spacing
Buildings | itu_brick/concrete/glass/metal/wood | Per-material PLY files
Roads | itu_asphalt | True widths, OS Open Roads
Water (River Trent) | itu_water (er=80) | OSM polygon
OSM/VOM Vegetation | itu_vegetation (er=17) | 20m disc spacing, 500 max/polygon
nDSM Extra Vegetation | itu_vegetation | Road verges, M1 motorway belt
Bridges & Railways | itu_concrete / itu_metal | man_made + highway bridges

## Slide 9
Vegetation Modelling Strategies
VEGETATION
Disc Geometry
Flat horizontal discs at canopy height
20m grid spacing within polygons
Sionna scatters rays off disc surface
Near-horiz. paths: near-zero cross-section
Max 500 discs per polygon
Three Vegetation Sources
OSM polygons: parks, forests, scrub
VOM polygons: LiDAR canopy (EA)
nDSM extra: verges, M1 motorway belt
Two-material terrain in veg zones
S=0 on terrain_veg (no scatter flood)
ITU-R P.833 Post-Correction
Weissberger formula applied post-RT
A = min(20, 0.187 x f^0.284 x d^0.588)
f in GHz, d = veg depth in metres
STRtree spatial index (O(n log n))
Handles bulk attenuation efficiently

## Slide 10
Ray Tracing Configuration
PARAMETERS
Parameter | Value
MAX_DEPTH | 8
NUM_SAMPLES_PS (cal) | 2M
NUM_SAMPLES_PS (eval) | 100M
Diffraction | True
Edge Diffraction | True
Scattering | True (ON mode)
CAL_MIN_DIST_KM | 0.15 km
CAL_MAX_DIST_KM | 1.50 km
TERRAIN_GRID_N | 1000x1000
MAX_DEPTH = 8
Optimal: >8 adds spatial noise, R2 drops
100M eval samples
Key insight: 90M/200M give identical R2
Calibration: 2M samples
Fast enough for Powell iteration (~28s/eval)
CAL_MIN_DIST = 0.15 km
Excludes 8 near-mast shadow receivers
CAL receivers: 208
0.15-1.50 km range (915 MHz campaign)

## Slide 11
Material Calibration via Powell Optimisation
CALIBRATION
1
Scalar Offset (Phase 0)
5M samples, ~28s - aligns mean PL level before material tuning
2
Sensitivity Probe
Verify materials produce non-zero path response (3-probe check)
3
Coord-Descent Warm-up
One-at-a-time parameter sweep to find good starting point
4
Powell Optimisation
scipy.optimize.minimize: fits er, sigma, S per material (30 DoF, 208 RX)
Free parameters: 10 materials x 3 (er, sigma, S) = 30 DoF
915 MHz Calibration
Cal receivers:
208 (0.15-1.50 km)
Cal RMSE floor:
~8-9 dB
Eval RMSE (100M):
6.0 dB
Best R2 @ 750m:
0.835
Scalar factor:
calibrated (Powell)
1802 MHz (in progress)
Before cal RMSE:
16.59 dB
After scalar (-8.8 dB):
14.05 dB
Powell target:
~12-13 dB

## Slide 12
RESULTS
915 MHz Simulation Results
Full scene | MAX_DEPTH = 8 | 100M eval samples | Powell-calibrated

## Slide 13
915 MHz Results: Full Scene (ON incoh, 100M samples)
RESULTS
Range | N | Bias (dB) | RMSE (dB) | R2
0-300m | 198 | +1.5 | ~9.0 | 0.007
0-500m | 385 | +0.9 | ~7.5 | 0.664
0-750m | 537 | +0.8 | 6.0 | 0.835
0-900m | 635 | +0.9 | ~6.8 | 0.797
0-1000m | 701 | +1.0 | ~6.5 | 0.813
0-1250m | 767 | +1.2 | ~7.2 | 0.741
Near-range R2~0 (0-300m): 8 mast-shadow LOS receivers — structural, not a calibration issue
Chart: 
| 0-300m | 0-500m | 0-750m | 0-900m | 0-1000m | 0-1250m
R2 | 0.007 | 0.664 | 0.835 | 0.797 | 0.813 | 0.741
R2 by Distance Range

## Slide 14
Impact of Scene Features on R2 (0-750 m)
SCENE EVOLUTION
Chart: 
| Buildings Only | +Vegetation | +Roads+ Water (cal) | Full Scene 2M samples | Full Scene 100M samples
R2 at 0-750m | 0.716 | 0.692 | 0.696 | 0.742 | 0.835
Best
Result
R2 = 0.835
+0.119
vs baseline
RMSE
6.0 dB
100M eval
samples

## Slide 15
Best Result Achieved
R2 = 0.835
RMSE = 6.0 dB | Bias = +0.8 dB
0-750 m range | N = 537 receivers | MAX_DEPTH = 8 | 100M evaluation samples
0-500m
R2=0.664
0-750m
R2=0.835
0-1000m
R2=0.813
0-1250m
R2=0.741

## Slide 16
Vegetation Disc Geometry: Hypothesis Test
VEGETATION ANALYSIS
Hypothesis: flat horizontal discs present near-zero cross-section to near-horizontal urban propagation rays, reducing effectiveness.
Experimental Design
DISABLE_VEG_DISCS = True
itu_ceiling_board set transparent (er=1, sigma=0, S=0)
Compare ON (discs) vs OFF (no discs)
Same calibration, same scene geometry
Result: Discs Are Active
ON avg_rays = 17,313 per receiver
OFF avg_rays = 60 per receiver
289x ratio confirms disc scattering
R2 with discs >= R2 without discs across all ranges
Conclusion: discs contribute via scattering (not blocking). Disc geometry + Weissberger post-correction architecture confirmed correct.

## Slide 17
Extension to 1802 MHz
1802 MHz
Scene Adaptations
itu_asphalt -> itu_very_dry_ground (Sionna registry)
itu_vegetation -> itu_ceiling_board (1802 MHz proxy)
VEG_SCATTERING_COEFF = 0.50
All geometry identical: same 23 PLY files
All 11 scene layers re-used without modification
Current Results (uncalibrated)
Range | N | RMSE (dB) | R2
0-750m | 537 | 11.8 | -0.050
0-1250m | 767 | 14.2 | +0.122
0-2500m | 1052 | 17.8 | -0.008
Status: Calibration In Progress
Bias of -5 to -9 dB = scalar offset dominated
Powell convergence expected: ~12-13 dB RMSE
915 MHz comparison planned post-calibration

## Slide 18
Key Findings
DISCUSSION
1
RT Matches Measurements Well
R2 = 0.835 at 0-750m. Comparable to best empirical models at 915 MHz in urban environments.
2
Scene Fidelity Matters
R2 rises from 0.716 (buildings only) to 0.835 (full scene + 100M samples). +0.119 R2 gain.
3
Vegetation Architecture Confirmed
Disc geometry + Weissberger post-correction is effective. Discs contribute via scattering, not blocking.
4
Sampling Density Is Critical
2M vs 100M eval samples: ~0.09-0.10 R2 difference. 100M is optimal; beyond yields no gain.

## Slide 19
Conclusions
CONCLUSIONS
High-fidelity 3D scene from open geodata (OSM, EA LiDAR, OS OpenData) achieves R2=0.835 at 0-750m, 915 MHz.
Powell-calibrated ITU-R P.2040-2 materials reduce uncalibrated RMSE from ~16 dB to 6.0 dB at 0-750m.
Full scene (terrain + buildings + vegetation + infrastructure) outperforms buildings-only baseline by +0.12 R2.
Vegetation disc geometry contributes positively via scattering; Weissberger ITU-R P.833 handles bulk attenuation.
100M evaluation samples provide optimal accuracy; beyond 100M yields no systematic R2 gain.
1802 MHz extension underway; calibration convergence of ~12-13 dB RMSE expected from Powell optimiser.

## Slide 20
Future Work
FUTURE WORK
Scene Improvement
OS road polygons (true widths)
TERRAIN_GRID_N > 1000
Additional building height data
Higher-res LiDAR integration
Modelling Advances
MAX_DEPTH > 8 for long-range paths
CAL_MIN_DIST optimisation study
Volume-based veg absorption (Sionna future)
Differentiable calibration via autodiff
Frequency Extension
1802 MHz calibration completion
Cross-frequency comparison (915/1802)
Potential 3.5 GHz / 26 GHz extension
Urban-rural scene comparison

## Slide 21
Acknowledgements
ACKNOWLEDGEMENTS
Data Sources
Ofcom: 2018 Nottingham 915 MHz & 1802 MHz measurement dataset
Environment Agency: EA LiDAR DTM/DSM (1m resolution)
OS OpenData + OpenStreetMap: road polygons, building footprints, land use
Software & Tools
Sionna RT 2.0 (NVIDIA Research) — GPU-accelerated ray tracing engine
Python ecosystem: NumPy, SciPy, Shapely, Fiona, GDAL, python-pptx
DrJIT: differentiable just-in-time compiler (MIT licence)
People & Funding
[Supervisor Name], [University / Department]
[Funding Body / Grant Reference]
[Research Group / Lab Name]

## Slide 22
Thank You
Questions Welcome
[Author Name] | [email@university.ac.uk] | [University]
Best R2
0.835
RMSE
6.0 dB
Range
0-750m
Freq
915 MHz