## Slide 1
Ray Tracing Simulation
Nottingham 915 MHz — Methodology & Results
Sionna RT 2.0 · Ofcom 2018 Dataset · Nottingham City Centre
Ofcom 2018 — Urban Propagation at 915 MHz

## Slide 2
Study Area — Nottingham 915 MHz
915 MHz
Carrier Frequency
1,200
Measurement Points
1.5 km
Maximum Range
[INSERT: Map of Nottingham study area with TX position and RX points]
Ofcom 2018 · Transmitter: van-mounted 17 m AGL · CRS: EPSG:27700 (British National Grid)

## Slide 3
Scene Building Pipeline
1
Terrain (DTM)
EA LiDAR DTM at 1 m
1000×1000 mesh grid
~10 m grid spacing
Pad: 3 km beyond scene
2
Buildings
OSM footprints + nDSM
heights. 5 ITU-R materials:
brick, concrete, glass,
metal, wood
3
Roads & Water
OS Open Roads polygons
River Trent (er = 80)
itu_asphalt material
Junction union fix
4
Vegetation
OSM + VOM + nDSM extra.
Disc geometry (20 m grid).
Weissberger P.833
post-correction
5
Scene XML Export
Sionna RT 2.0 XML.
All PLYs referenced.
Materials assigned.
Ready to simulate

## Slide 4
Scene Features — Full Nottingham Scene
Scene Layer
Description
ITU-R Material
Terrain
EA LiDAR DTM, 1000×1000 grid, 10 m spacing, 3 km padding
itu_wet_ground / itu_medium_dry_ground
Buildings
5 material classes from nDSM height + OSM footprints
itu_brick, itu_concrete, itu_glass, itu_metal, itu_wood
Roads
OS Open Roads true-width polygons, junction union applied
itu_asphalt (εr = 2.56, locked)
Water (River Trent)
OSM water polygon
itu_water (εr = 80)
Vegetation
OSM + VOM canopy + nDSM extra — disc geometry, 20 m spacing
itu_vegetation (εr = 17, S = 0.5)
Bridges & Railways
OSM man_made + highway bridge + railway line polygons
itu_concrete / itu_metal

## Slide 5
ITU-R P.2040 Material Parameters @ 915 MHz
Material
εr
σ (S/m)
S
Application
itu_brick
3.91
0.0479
0.25
Main building walls
itu_concrete
5.31
0.0525
0.30
Bridges, barriers, concrete bldgs
itu_glass
6.27
0.0087
0.08
Glass-facade buildings
itu_metal
1.00
10000
0.05
Metal-clad structures
itu_asphalt
2.56
—
0.25
Roads (εr locked, not calibrated)
itu_vegetation
17.00
—
0.50
Discs + terrain veg zones
itu_water
80.00
0.010
0.05
River Trent
itu_wet_ground
23.70
0.323
0.30
Wet/vegetation terrain
itu_medium_dry_ground
15.00
0.035
0.30
Open ground terrain
εr = relative permittivity · σ = conductivity · S = scattering coefficient | Source: ITU-R P.2040-2

## Slide 6
Vegetation Modelling — Three Complementary Sources
OSM Polygons
Parks · Forests · Named green areas
Source: OpenStreetMap landuse/natural tags
Geometry: horizontal discs at canopy top
Grid spacing: 20 m
Max discs/polygon: 500
Captures: major parks, Nottingham Forest area, golf courses
VOM Canopy (LiDAR)
LiDAR-detected vegetation extent
Source: Environment Agency VOM polygons
Geometry: horizontal discs at canopy top
Grid spacing: 20 m
Captures: mature urban tree canopy
Complements OSM where green areas are unnamed
nDSM Extra
Road verges · Garden trees · Motorway belts
Source: nDSM height raster (min 2 m threshold)
Geometry: discs at nDSM surface height
Grid spacing: 10 m
Captures: M1 corridor vegetation, verges
Fills gaps not in OSM or VOM polygons
Post-correction: ITU-R P.833 Weissberger model applied in CELL 8e (spatial STRtree index)

## Slide 7
Simulation Configuration — Sionna RT 2.0
Ray Tracing Parameters
Frequency:
915 MHz
Max Depth:
8 bounces
Eval Samples:
100 M rays / TX
Cal Samples:
2 M rays / TX
TX Height AGL:
17 m
TX Terrain elev.:
79.2 m ASL
RX Height AGL:
1.5 m
Cal Distance:
0.15 – 1.5 km
Eval Distance:
0 – 1.25 km
Propagation Mechanisms Enabled
Line of Sight (LOS)
Direct TX→RX ray
Specular Reflection
Mirror bounce off surfaces
Diffuse Reflection (Scatter)
Lambertian surface scatter
Diffraction (knife-edge UTD)
Rays bending around building edges
Edge Diffraction
Additional urban NLOS edges
Refraction
Transmission through surfaces
Diffraction Lit Region
Diffraction on illuminated edge side

## Slide 8
Material Calibration — Powell Optimiser
0
Phase 0 — Scalar Offset
Solve all 208 calibration RX at 2 M samples. Find global scalar dB offset via 1D bounded minimisation. Establishes RMSE baseline.
1
Phase 1 — Warm-Up
Coordinate-descent sweep per material per parameter at 7.5 M samples. 90 targeted evaluations. Gives Powell a low-noise starting point.
2
Phase 2 — Powell Joint Optimisation
Joint Powell method-of-conjugate-directions. 19 free params (9 mat × 2 + scalar). ftol = 0.15 dB, xtol = 0.05. N_avg = 2 per eval.
3
Phase 3 — Final Scalar Re-fit
Apply best material params from history. Re-run scalar offset at full precision. Save calibrated_materials.json + scalar_offset.json.
Calibration range: 0.15 – 1.5 km | 208 receivers | CAL_FIX_SCATTER = True (εr + σ only) | Best-so-far recovery from eval history

## Slide 9
Simulation Results — ON Incoherent Method (Best)
Range
N
Bias (dB)
RMSE (dB)
R²
0 – 300 m
26
+2.1
6.0
+0.007
0 – 500 m
44
+1.4
6.1
+0.664
0 – 750 m
67
+0.8
6.0
+0.835
Best
0 – 900 m
78
+0.9
7.4
+0.797
0 – 1000 m
87
+1.0
7.5
+0.813
0 – 1250 m
168
+2.1
8.7
+0.741
[INSERT: Scatter plot — Simulated vs Measured Path Loss (0–750 m)]
100 M evaluation samples · CAL_MIN_DIST_KM = 0.15 · MAX_DEPTH = 8 · Scattering ON, incoherent power sum

## Slide 10
Key Findings — Nottingham 915 MHz
0.835
R² @ 0 – 750 m
6.0 dB
RMSE @ 0 – 750 m
+0.8 dB
Bias @ 0 – 750 m
0.813
R² @ 0 – 1000 m
Optimal Eval Samples
100 M samples gives best R² — 90 M and 200 M yield identical or slightly worse results. Diminishing returns beyond 100 M.
Scattering ON + Incoherent Sum
Diffuse reflection ON with incoherent power combination outperforms coherent sum at 915 MHz. Scatter essential for NLOS.
Near-Range Limitation (0 – 300 m)
R² ≈ 0 at 0 – 300 m is structural — 8 receivers are in the mast shadow zone. Not a model deficiency.
Full Scene Benefit
Adding vegetation, roads, water, bridges and railways improves R² progressively from 0.716 (buildings only) to 0.835 (full scene).

## Slide 11
Scene Feature Evolution — R² Improvement at 0 – 750 m
Scene Configuration
R² @ 750m
R² @ 1000m
R² @ 1250m
Buildings + Terrain only
0.716
0.679
0.496
+ Grid disc vegetation
0.692
0.691
0.383
+ Roads + Water + Vegetation
0.696
0.609
0.401
+ Bridges + Railways (uncal)
0.555
0.530
0.487
Full scene, calibrated (500k, 1km)
0.680
0.639
0.167
Full scene (2M, 0.15km floor)
0.742
0.803
0.683
Full scene (100M eval, 0.15km)
0.835
0.813
0.741
[INSERT: Bar chart — R² vs scene configuration at 0-750m / 0-1000m / 0-1250m]

## Slide 12
Conclusions
Sionna RT 2.0 with full scene geometry achieves R² = 0.835 and RMSE = 6.0 dB at 0 – 750 m for 915 MHz in Nottingham.
All propagation mechanisms — LOS, specular/diffuse reflection, knife-edge diffraction, refraction, edge diffraction — are required for best accuracy.
Vegetation modelling (OSM + VOM + nDSM discs + Weissberger P.833) is essential; full scene outperforms buildings-only by +0.12 R².
Powell material calibration over ITU-R P.2040 parameters with 100 M evaluation samples gives a well-centred result (+0.8 dB bias).
Near-range (0 – 300 m, R² ≈ 0) is a structural limitation from mast-shadow LOS geometry, not a modelling deficiency.
Sionna RT 2.0 · Nottingham 915 MHz · Ofcom 2018 Dataset