## Slide 1
Ray Tracing for Path Loss Prediction
in Urban Environments
Scene
Nottingham · Ofcom 2018 Drive Test
Frequency
915.95 MHz (IoT / LoRaWAN band)
Tool
Sionna RT 2.0 + Sionna 0.19 Differentiable RT
Goal
Minimise RMSE against 1 200 real Ofcom measurements
[ Scene Render or Coverage Map ]
1 / 12

## Slide 2
MOTIVATION
2 / 12
Purpose & Motivation
⚠ The Problem
› Empirical models (COST-231, Okumura-Hata) give 20–36 dB errors
› No terrain, no building geometry, no material physics
› Fixed-environment formulas — break in new cities
🎯 Our Goal
› Minimise RMSE against 1 200 real Ofcom measurements
› Reproduce physical propagation: diffraction, reflection, scatter
› Differentiable RT calibration (NVLabs Hoydis et al. 2023)
📡 The Dataset
› Ofcom 2018 drive test 915.95 MHz, Nottingham UK
› 1 200 receivers | 0.3–9 km
› RSSI range: −118 to −23 dBm Noise floor: −124 dBm

## Slide 3
RESEARCH QUESTIONS
3 / 12
Research Questions
RQ 1
Flat Terrain vs DEM
How much does digital elevation modelling (DEM) improve path loss prediction accuracy over a flat z = 0 scene in Nottingham?
RQ 2
Differentiable RT Calibration
Can Sionna 0.19 differentiable RT (NVLabs approach) achieve < 5 dB RMSE on the Ofcom 2018 UK dataset after calibration?
RQ 3
Optimal Scene Configuration
Which combination of scene geometry, material parameters, and ray-tracing settings best represents urban Nottingham at 915 MHz?

## Slide 4
METHODOLOGY
4 / 12
Simulation & Calibration Pipeline
01
INPUT DATA
OSM + EA LiDAR + Ofcom CSV
▶
02
SCENE BUILDER
nDSM + ITU-R P.2040-2 + Terrain PLY
▶
03
RAY TRACING
Sionna 2.0 PathSolver + Sionna 0.19 Diff RT
▶
04
CALIBRATION
Scalar (Cell 10b) Material (Cell 11b)
▶
05
ML RESIDUAL
ResidualMLP (Cell 15) CNN+MLP (Cell 14) MaterialMLP (Cell 16)
▶
06
VALIDATION
RMSE · MAE · Bias STD · R² per band
Output Metrics per Distance Band: RMSE | MAE | Bias | STD | R²

## Slide 5
INPUT DATA
5 / 12
Ofcom Dataset — GPS to Sionna Receivers
1
Raw Ofcom CSV
GPS (WGS84 lat/lon) + RSSI (dBm) per measurement point
2
Filter & Clean
Keep 915.95 MHz · drop RSSI < −124 dBm · remove duplicates
3
Coordinate Transform
WGS84 → UTM Zone 30N (EPSG:32630) → local scene XY (metres)
4
Height Assignment
RX Z = EA LiDAR DTM elevation + 1.5 m AGL
5
Sionna RX Array
Each point → Receiver object · isotropic antenna · 1 200 total
6
PL Reference
PL_meas = TX_EIRP − RSSI_meas (dB) → ground truth for RMSE
Key Numbers
Raw Ofcom points
~4 000
After filtering
1 200 receivers
Coverage range
0.3 km – 9 km from TX
TX location
(−1.2559°, 52.9863°)
TX height
17 m AGL
Frequency
915.95 MHz
RSSI range (meas)
−118 to −22.9 dBm
Noise floor
−124 dBm
PL_meas range
93.7 – 142.4 dB

## Slide 6
SCENE CONSTRUCTION
6 / 12
Scene Construction — Blender → OSM → Merged PLY
Stage 1 · Blender (Flat)
Manual · OSM importer plugin
✔ Pros
Fast to build — one import/export
Full geometry cleanup in GUI
Single merged PLY → Sionna loads in seconds
✘ Cons
No terrain — flat z=0 plane
Nottingham hills completely absent
Manual — not reproducible
8–15 dB error at 300–1500 m
Stage 2 · OSM Direct (DEM)
Automated · Python OSMnx + scene builder
✔ Pros
Fully automated & reproducible
ITU-R P.2040-2 materials per building type
Real terrain from EA LiDAR (2 m res)
✘ Cons
OSM heights often missing → estimated
OSM tags inconsistent across Nottingham
Longer scene build time
Stage 3 · Merged PLY
Why we merged 150 k files → one per material
✔ Pros
Scene load: 20 min → 45 sec
Single BVH → 50× faster ray traversal
No GPU memory fragmentation
Solve rate improved directly
✘ Cons
Per-material merge requires preprocessing
Harder to inspect individual buildings

## Slide 7
ERROR SOURCES
7 / 12
Known Error Sources — Building Heights & Terrain Geometry
Building Height Problem — Both Scenes
OSM height tag
Only ~30% of buildings have it
70% use estimate
building:levels tag
height = levels × 3 m
Wrong for mixed-use
No tag
Default 8 m applied
Underestimates tall buildings
Industrial/warehouse
Tagged as residential
Wrong shadowing
→ Wrong building heights = wrong diffraction angles = wrong path loss
Flat Terrain Errors (Sionna v1)
Terrain missing
All buildings on z=0
+8–15 dB overestimate 300–1500 m
Ground reflection
Flat plane — wrong angle
~3–5 dB additional bias
RX height
1.5 m above z=0, not real ground
Some RX inside terrain
DEM Terrain Errors (Sionna v2)
Building heights
DEM fixes ground Z, not building tops
Residual ±3–8 dB
DEM resolution
2 m — small walls/hedges missed
Minor
Roof geometry
Flat-roof box — no pitched roofs
Diffraction angle error
Key Takeaway
Flat terrain: dominant error is missing hills → systematic bias DEM terrain: dominant error is building height estimation → random scatter Both improve with material calibration — but building height is a hard geometric limit

## Slide 8
ELEVATION DATA
8 / 12
Elevation Data Sources — DTM, DSM & nDSM
DTM
Digital Terrain Model
Captures
Bare earth only (ground, roads, rivers)
Source
EA LiDAR 1m (last / ground returns)
Use in scene
Terrain mesh PLY → correct RX ground Z
Limitation
No buildings or trees
DSM
Digital Surface Model
Captures
Everything — ground + buildings + trees
Source
EA LiDAR 1m (first returns)
Use in scene
Building height estimation
Limitation
Cannot separate building from terrain directly
nDSM
Normalised DSM = DSM − DTM
Captures
Height of objects ABOVE ground only
Source
Derived: DSM − DTM
Use in scene
Accurate per-building AGL height from LiDAR
Limitation
Requires both DTM & DSM
nDSM = DSM − DTM → object height above ground (buildings, trees)

## Slide 9
RESULTS COMPARISON
9 / 12
RMSE Results — Flat / DTM / nDSM Scene Comparison
Scene Config
Terrain
Building Heights
RMSE
Bias
Key Issue
Flat z=0 (Sionna v1)
None — z=0 plane
OSM estimate / default 8 m
19.6 dB
−4.4 dB
Missing hills → +8–15 dB overestimate at 300–1500 m
DTM terrain (Sionna v2)
EA LiDAR DTM ✅
OSM floor count / default 8 m
14.1 dB
~0 dB
Building height estimation still introduces ±3–8 dB scatter
nDSM heights (2.8–6 GHz)
EA LiDAR DTM ✅
LiDAR nDSM (accurate AGL)
Used in 2.8 GHz scene
—
Rooftop equip added — only valid at higher frequencies
Key Finding: DTM terrain alone reduces RMSE by 5.5 dB (19.6 → 14.1 dB). Bias drops from −4.4 dB → ~0 dB. Terrain is essential — building height remains the next bottleneck.

## Slide 10
SCENE PIPELINE
10 / 12
Final Scene: scene_v2_infra — How DTM + nDSM Are Merged
EA LiDAR DTM 1m
Ground-only elevation raster (GeoTIFF) Covered: 11×11 km Nottingham bbox
▼
EA LiDAR DSM 1m
First-return surface raster Includes buildings + trees
▼
nDSM = DSM − DTM
Per-pixel height above ground Median filter → remove LiDAR spikes
▼
OSM Footprints
Building polygons + landuse tags Height assigned from nDSM median under footprint
▼
scene_v2_infra
terrain.ply (DTM mesh) + building meshes + road/veg/infra + ITU-R P.2040-2 materials
▼
What Each Layer Contributes
DTM terrain
Correct ground Z → RX at real AGL
8–15 dB bias removed
nDSM heights
Accurate building heights from LiDAR
Correct diffraction angles
OSM footprints
Building positions and 2D shapes
3D geometry
ITU materials
EM properties per surface type
Physical reflection/scatter

## Slide 11
RAY TRACING SETUP
11 / 12
Ray Tracing Configuration — Mechanisms & Parameters
Ray Mechanisms
✔
LOS
Direct path TX → RX
✔
Specular Reflection
Building face bounce
✔
Diffraction
Over rooftops / wedge edges
✔
Edge Diffraction
Around building corners — dominant NLOS
✔
Scattering
Lambertian rough surface diffuse
72% of rays are diffraction — edge diffraction is the dominant propagation mechanism in urban Nottingham NLOS at 915 MHz
Solver Parameters
Frequency
915.95 MHz
MAX_DEPTH
7 (up to 7 bounces)
NUM_SAMPLES
10 000 000 (NVLabs approach)
TX height
17 m AGL (mast)
RX height
1.5 m AGL (IoT device)
TX antenna
Dipole — donut pattern
RX antenna
Isotropic
Noise floor
−124 dBm
BATCH
1 receiver per solve (NVLabs)

## Slide 12
OSM FEATURES
12 / 12
OSM Features Downloaded — Role in Propagation Physics
Feature Classes Downloaded
Buildings
building=*
52 248
Brick/Concrete/Glass/Metal/Wood
Roads
highway=*
Full net
Asphalt
Trees/Vegetation
natural=tree, landuse=forest
~273
Vegetation
Masts/Towers
man_made=mast/tower
100s
Metal
Power pylons
power=tower
100s
Metal
Railways
railway=rail
Full net
Metal
Water bodies
natural=water, waterway=*
Polygons
Water
Barriers/embank.
barrier=*, embankment
Many
Concrete
Car parks
amenity=parking
Many
Concrete
Propagation Impact per Feature
Buildings
Diffraction + reflection — dominant NLOS loss
Primary
Metal masts
Strong specular reflectors — secondary paths
+2–5 dB
Roads
Ground bounce — 2-ray interference pattern
±3 dB
Vegetation
Absorption + scatter (P.833) up to 67 dB at 9 km
+12–27 dB
Railways
Specular waveguide along rail corridors
Elevated
Water (Trent)
Near-specular reflection — local enhancement
Local +
Barriers
Extra diffraction edges — additional shielding
+2–8 dB
Metal infrastructure (σ = 10⁷ S/m) added in scene_v2_infra — absent in flat baseline. At 915 MHz metal surfaces are near-perfect reflectors creating strong secondary paths.

## Slide 13
TX / RX SETUP
13 / 12
TX & RX Placement — GPS to Scene + Ray-Cast Validation
TX — Transmitter
GPS (WGS84)
−1.25590°, 52.98630°
Transform
WGS84 → UTM 30N → scene XY
Terrain Z
~79 m ODN (EA LiDAR DTM)
AGL height
+17 m (mast)
Scene Z
~96 m absolute
Antenna
Dipole — donut pattern
Ray-cast check
Downward ray → above terrain ✅
RX — 1200 Ofcom Receivers
1
GPS (WGS84)
→ UTM Zone 30N (EPSG:32630) → local scene XY
2
DEM lookup
Bilinear interpolation at (x,y) → terrain Z from LiDAR DTM
3
Height assignment
RX Z = terrain Z + 1.5 m AGL
4
Ray-cast check
Shoot ray downward → if first hit above RX → inside building
5
Fix if invalid
Raise RX to building roof + 0.1 m OR exclude from solve
Why Positioning Validation Matters
RX inside building footprint
Spawned in solid geometry → no paths → NaN RSSI
Ray-cast detects → adjust Z
TX near building face
Rays immediately blocked → unrealistic near-field
Minimum clearance check
DEM returns 0 at scene edge
RX at z=1.5 m → inside terrain → all paths blocked
Fallback to median terrain Z
Ofcom GPS imprecision ±3–10 m
RX may be on wrong side of building wall
Accepted — statistical uncertainty

## Slide 14
LOS / NLOS
14 / 12
Receiver Classification — LOS vs NLOS
Classification & Results
Method: LOS if direct path amplitude |a_LOS|² > 0 in solved paths
LOS
~20
1.7%
< 200 m · open streets
NLOS
~1120
98.3%
All ranges · urban canyon
Ray Type Breakdown — 153 450 total rays
Diffraction 110 618 (72.1%)
Multi-reflection 37 006 (24.1%)
Reflection 3 190 (2.1%)
LOS 2 636 (1.7%)
Why It Matters for Path Loss Modelling
LOS
Free-space + ground reflection Friis equation sufficient
NLOS < 500 m
Diffraction over 1–2 rooftops Edge diffraction critical
NLOS 500–2000 m
Multi-hop diffraction + scatter Full ray tracing essential
NLOS > 2000 m
Statistical scatter paths 10M+ samples needed
98.3% NLOS — empirical models calibrated for mixed LOS/NLOS are fundamentally mismatched. Ray tracing is necessary.

## Slide 15
CALIBRATION · STAGE 1
15 / 12
Stage 1 — Scalar Offset Calibration (NVLabs ITU Materials Baseline)
Method
1
Pre-trace all receivers once — cache RSSI (no gradient — offline)
2
Ghost path filter: remove PL_sim > PL_meas_max + 10 dB (physically impossible multi-bounce paths)
3
Single trainable scalar: scaling_factor_db Minimise SMAPE loss on linear power (NVLabs standard)
4
Best-RMSE checkpoint — save scalar at lowest RMSE step (not SMAPE-final — prevents overshoot)
Reference: Hoydis et al. 2023 (arXiv:2311.18558) — ITU Materials scalar baseline
Results
Receivers solved
383 / 1140 (34%)
Valid pairs after filter
218
Ghost paths removed
165 (PL > 154.4 dB)
Pre-calibration RMSE
14.12 dB ✅
Best-RMSE scalar
−0.50 dB (≈ 0)
Post-calibration RMSE
14.43 dB
RMSE improvement
−0.31 dB
Best scalar ≈ 0 dB — scene_v2_infra + DEM is already physically well-calibrated. Scalar stage validates, not corrects.

## Slide 16
CALIBRATION · STAGE 2
16 / 12
Stage 2 — Differentiable Material Calibration (Full NVLabs)
Method
Trainable params
17 materials × 3 vars (εᵣ, σ, S) = 51 parameters
Gradient flow
compute_fields() inside GradientTape → fully differentiable through RT
Loss
SMAPE on linear power + Tikhonov regularisation → ITU-R P.2040-2
Optimizer
Adam LR=0.05 → cosine decay → 0.001
Steps
300
Baseline
Initialised at ITU-R P.2040-2 Table 3 values
17 Materials — ITU-R P.2040-2 Initial Values
Material
εᵣ
σ (S/m)
S
itu_concrete
5.31
0.0304
0.30
itu_brick
3.91
0.0238
0.25
itu_glass
6.27
0.0039
0.08
itu_metal
1.00
1.0×10⁷
0.05
itu_asphalt
2.56
0.0050
0.30
itu_vegetation
1.50
0.0019
0.40
itu_wet_ground
31.07
0.1338
0.35
itu_water
80.00
0.0100
0.03
itu_wood
1.99
0.0043
0.15
Target: RMSE < 10 dB (from 14.12 dB baseline)

## Slide 17
ANTENNA CONFIG
17 / 12
Antenna Configuration — TX & RX Specifications
TX — Transmitter Antenna
Type
Collinear omni (simulated as dipole)
Pattern
Donut — omni in azimuth, null at zenith
Gain
1.3 dBi
Polarisation
Vertical
Height
17 m AGL on mast
Sionna model
pattern='dipole'
Conducted power
49.0 dBm
EIRP
49.0 + 1.3 = 50.3 dBm
RX — Receiver Antenna
Type
Isotropic
Pattern
Uniform — equal gain all directions
Gain
0 dBi
Height
1.5 m AGL (IoT device)
Sionna model
pattern='iso'
Noise floor
−124 dBm
Why These Choices
TX dipole (not iso)
Real Ofcom mast uses collinear omni — donut pattern matches real radiation shape
RX isotropic
IoT devices vary widely in orientation → iso avoids assuming device direction
RX iso = Sionna 2.0
Cross-notebook consistency — both use same RX model for fair comparison
Noise −124 dBm
Covers full Ofcom RSSI range (−118 to −22.9 dBm) — no valid meas. excluded