## Slide 1
Sionna 0.19.2 Ray-Tracing
Nottingham Urban Scene · 3602.5 MHz · 4001 Ofcom Drive-Test Points
Project Milestones · Failures & Fixes · Scene Enhancements
FYP 2026 · Sionna RT + AWS DEM + OSM + Overture Maps + Meta CHM

## Slide 2
Project Overview
Goal
▶ Simulate urban radio propagation
▶ Nottingham city, 10.7 × 11.2 km
▶ 3602.5 MHz (5G NR n78 band)
▶ Compare vs 4001 Ofcom RSSI points
▶ No bias / correction factors
RF Parameters
TX conducted power: 45.0 dBm
EIRP: 54.0 dBm (9 dBi antenna)
RX extra gain: 18.0 dB (LNA)
Noise floor: −109 dBm (Ofcom)
SITE_CORRECTION_DB = 0.0
Simulation Engine
Sionna 0.19.2 (TF 2.15 + Mitsuba 3)
SBR path solver (GPU: cuda_ad_rgb)
MAX_DEPTH = 10 bounces
NUM_SAMPLES_CM = 200M rays
NUM_SAMPLES_PS = 10M / batch

## Slide 3
Scene Evolution — Saved Checkpoints
CP 1 Flat Terrain + OSM Buildings
• 95k individual PLY files
• 8 merged PLY shapes
• Flat ground z=0
• itu_wet_ground material
→
CP 2 AWS DEM Terrain
• 72 GeoTIFF tiles (zoom-14)
• 500×500 terrain grid
• Z range: −34 → +87 m
• Bilinear interpolation
→
CP 3 Overture Maps Building Heights
• 70,765 buildings fetched
• 22,558 heights enriched
• Fallback: OSM levels×3.5m
• Default: 8.0 m
→
CP 4 Meta CHM Tree Geometry
• Quadkey zoom-9 tiles
• Tile 031311330 (1–53 m)
• 115,497 tree cylinders
• 89 MB binary PLY

## Slide 4
Key Failures & Fixes
✗ Flat PL-FSPL = +10.3 dB at ALL distances
Cause: itu_wet_ground (ε=30) created strong specular bounces dominating all paths
✓ Fix: Switched to itu_urban_ground (ε=5, σ=0.5) — absorbs ground reflections
✗ Meta CHM HTTP 404 (lat_lon.tif naming)
Cause: Tiles use Web Mercator quadkey zoom-9 format, not degree-grid lat/lon
✓ Fix: Implemented _latlon_to_quadkey() — Nottingham = tile 031311330
✗ OOM: two 65536×65536 CHM tiles = 32 GB RAM
Cause: Loading full tiles before mosaic killed the kernel
✓ Fix: Windowed reads: clip each tile to scene bbox before loading (~18 MB each)
✗ 0 trees placed despite valid CHM data
Cause: Manual mosaic row-offset bug + 26M-point Python loop (hours to run)
✓ Fix: Vectorised numpy meshgrid in Mercator coords, per-strip direct indexing
✗ 95,185 PLY files crashed scene.xml (12 MB)
Cause: Individual bld_XXXXX_wall/roof.ply for each OSM building
✓ Fix: Merged by material → 8 PLY files (wall_itu_brick.ply etc.)
✗ NaN tag bug: 95% of buildings got wrong material
Cause: str(NaN)='nan' is truthy — if off: return 'itu_glass' fired everywhere
✓ Fix: Added _tag() helper converting 'nan'/'none' strings to empty string

## Slide 5
Coverage Analysis & Ray Tracing Parameters
Why 11% Coverage?
Scene: 10.76 × 11.25 km = 121 km²
TX position: (4711, 3074) m from centre
TX near NE edge of scene bbox
3.6 GHz urban macro cell radius ≈ 2 km
π × 2² / 121 km² ≈ 10.4%
Simulated coverage: 11.0% ✓ matches
NOT a bug — single cell on large scene
Drive-test points ARE within covered area
Ray Tracing Settings
MAX_DEPTH = 10 bounces
(was 6 → added NLOS at 500–1200 m)
NUM_SAMPLES_CM = 200M
GPU: 100 runs × 2M rays
NUM_SAMPLES_PS = 10M / batch
Path solver per receiver batch
scat_keep_prob = 0.001
Scatter rays: 1 in 1000 kept
GRID_SIZE_M = 10 m
167 rays/cell (borderline for NLOS)
Scatter Impact
With scatter: mean=−55.6 dBm
Without scatter: mean=−55.5 dBm
Scatter impact std = 7.06 dB
(±7 dB per-cell redistribution)
mean ≈ 0 dB = energy conservation ✓
Scatter active only after Cell 33
(re-apply S coeff after scene load)
CAL_MAX_DEPTH must match MAX_DEPTH
(was 6, should be 10)

## Slide 6
Scene Enhancements — Final Architecture
AWS Elevation Tiles
• Zoom-14 GeoTIFF tiles (~5.8 m/px)
• 72 tiles downloaded & mosaiced
• Bilinear interpolation for smooth mesh
• DEM range: −34 to +102 m local
• 500×500 terrain grid (~9 MB PLY)
OSM + Overture Buildings
• 61,985 OSM building footprints
• 70,765 Overture Maps entries
• 22,558 real heights enriched
• Fallback: levels×3.5 m or 8 m default
• 47,592 buildings processed → 8 PLY files
Meta AI Canopy Height
• Quadkey zoom-9 Web Mercator tiles
• 1 m resolution CHM (windowed read)
• Height range: 1–53 m in Nottingham
• 115,497 trees at 20 m grid spacing
• 8-sided cylinders, binary PLY (87 MB)
ITU-R P.2040-2 Materials
• itu_brick S=0.30, itu_concrete S=0.40
• itu_glass S=0.08, itu_metal S=0.05
• itu_vegetation S=0.75 (highest scatter)
• itu_urban_ground ε=5 σ=0.5
• LambertianPattern on all materials

## Slide 7
Remaining Issues & Next Steps
Known Issues
✗ CAL_MAX_DEPTH=6 ≠ MAX_DEPTH=10 → calibrated S values are for depth=6
✗ TREE_GRID_SPACING was 5 m → 1.8M trees → 1.5 GB PLY → kernel OOM
✗ FLAT_TERRAIN=True still in Cell 0c → TX at z=17m not z=25m
✗ Scatter S=0 if Cell 33 not re-run after kernel restart
✗ Scene centred on bbox not TX → TX at (4711, 3074) near NE edge
Next Steps
▶ Set FLAT_TERRAIN=False in Cell 0c → TX Z should show ≈25 m
▶ Run Cell 33 after every scene load → confirm S≠0 in Cell 34
▶ Fix CAL_MAX_DEPTH=10 → re-run calibration sweep for valid S values
▶ Run Cell 9b → get bias/RMSE vs 4001 Ofcom drive-test points
▶ Consider re-centering scene bbox on TX location for better coverage %
▶ Increase scat_keep_prob 0.001→0.01 for better NLOS scatter at 500m+